## Slide 1: DeviceMaster® UP
Data Protocol Solutions from Comtrol Corporation
and

## Slide 2: DeviceMaster UP Product Overview
Protocol flexibility — EtherNet/IP, Modbus/TCP, Modbus RTU/ASCII, PROFINET IO
Connectivity to both serial and Ethernet TCP/IP devices
Available models — 1-port, 2-port 1E, 2-Port 2E, 4-port, and embedded
Rugged housing—with panel, rack, and DIN rail mounting options
Daisy Chaining — on select models, use of dual Ethernet ports for daisy chaining network connections between multiple units
Variable power input — eliminates the need for power converters
Temperature rated for extreme conditions — operating temperature of –37° to 74°C enables DeviceMaster UP to function in a wide variety of harsh environments
Industrial Ethernet Connectivity

## Slide 3: DeviceMaster® UP
EtherNet/IP
Profinet IO
Modbus
  3 major firmware builds
    Modbus Server*
    Modbus Router
    Modbus TCP
NS Link* and SocketServer*
“Universal Protocol”
*Can also run on DeviceMaster ® RTS hardware

## Slide 4: DeviceMaster® RTS
Connecting Serial to Ethernet
NS Link Firmware
Additional “like native” COM ports appear.
Micrologix (or other PLC that can be programmed through it’s serial port)

## Slide 5: DeviceMaster® RTS
A large factory may have a huge variety of sensors, instruments, devices, PLCs, and Industrial Computers. More often than not, they are of mixed heritage.

## Slide 6: DeviceMaster® RTS
Remote programming can increase safety, comfort, and uptime.

## Slide 7: DeviceMaster® RTS
Connecting Serial to Ethernet
NS Link Firmware – Installation Summary

## Slide 8: DeviceMaster® RTS
Connecting Serial to Ethernet
NS Link Firmware – Installation Summary

## Slide 9: DeviceMaster® RTS
Connecting Serial to Ethernet
NS Link Firmware – Installation Summary

## Slide 10: DeviceMaster® RTS
Connecting Serial to Ethernet
Socket Server Firmware
Data appears on a socket port.

## Slide 11: DeviceMaster® UP
Data Protocol Solutions from Comtrol Corporation

## Slide 12
EtherNet/IP Firmware
Ethernet/IP to serial and Ethernet TCP/IP raw/ASCII devices

## Slide 13
EtherNet/IP Firmware
• Connectivity – Ethernet/IP to serial and Ethernet TCP/IP raw/ASCII devices • Low-latency updates of received packets to PLC memory. Typically less than 10 ms • Connectivity to high-speed devices. Supports message rates as high as 50 updates per second when receive mode is configured to Write-to-Tag/File
• Large received packet support – up to 1518 bytes serial and 2048 bytes Ethernet TCP/IP
• Received packet size control – truncate or drop oversized packets
• Message Throttling – ensures PLC can process each received data packet
• Intelligent packet identification – start and end of transmission character detection/appending
• Three methods of receive communication to the PLC – Write-to-Tag/File, Write-to-Tag/File-Synced, and Polling
• Vendor Specific CIP objects – configuration, data transfer, and statistics

## Slide 14
EtherNet/IP Firmware: Specific Configuration Example
How would I configure this?

## Slide 15
EtherNet/IP Firmware: Specific Configuration Example
How would I configure this?
[Establish that your PLC and Devicemaster can see each other.]

## Slide 16
EtherNet/IP Firmware: Specific Configuration Example
How would I configure this?
Write your own PLC logic, or borrow/use/ keep/modify our examples provided on the CD with every Devicemaster

## Slide 17
How would I configure this?
EtherNet/IP Firmware: Specific Configuration Example

## Slide 18
EtherNet/IP Firmware: Specific Configuration Example

## Slide 19
EtherNet/IP Firmware: Specific Configuration Example

## Slide 20
How would I configure this?
EtherNet/IP Firmware: Specific Configuration Example

## Slide 21
EtherNet/IP Firmware: Specific Configuration Example
How would I configure this?
In the DMUP, for each path you can specify which data tag to write to. The payload will be prepended by two registers showing sequence # and length (bytes).

## Slide 22
EtherNet/IP Firmware: Specific Configuration Example
How would I configure this?

## Slide 23
EtherNet/IP Firmware: Specific Configuration Example
How would I configure this?
Configure the appropriate serial port settings for the LK-G5000 RJ11 RS232C. There are many valid choices that will work for the LK-G and the DeviceMaster UP

## Slide 24
EtherNet/IP Firmware: Specific Configuration Example
How would I configure this?
Using the pinouts referenced in manuals for both devices, create cabling that matches up the proper pins on both ends of the serial connection. In my case, I cut an RJ11 cable and a standard DB9 cable and spliced the three necessary wires together. (Custom cable.)

## Slide 25
How would I configure this?
EtherNet/IP Firmware: Specific Configuration Example

## Slide 26
How would I configure this?
EtherNet/IP Firmware: Specific Configuration Example

## Slide 27
EtherNet/IP Firmware: Specific Configuration Example

## Slide 28
EtherNet/IP Firmware: Specific Configuration Example

## Slide 29
How would I configure this?
EtherNet/IP Firmware: Specific Configuration Example

## Slide 30
EtherNet/IP Firmware: Specific Configuration Example
How would I configure this?
Write your own PLC logic, or borrow/use/ keep/modify our examples provided on the CD with every Devicemaster

## Slide 31
EtherNet/IP Firmware: Specific Configuration Example
How would I configure this?
Write your own PLC logic, or borrow/use/ keep/modify our examples provided on the CD with every Devicemaster

## Slide 32
EtherNet/IP Firmware: Specific Configuration Example
How would I configure this?
Put outbound data (writes) in the write block of registers, and the data returned by the LK-G5000 will be automatically written into the read block of registers specified in DMUP

## Slide 33
EtherNet/IP Firmware: Specific Configuration Example
How would I configure this?
Using Dual Connect: Open a telnet or hyperterminal session (or other TCP/IP test tool) to view the plain ASCII data over a TCP port (specified by you in DMUP)

## Slide 34
EtherNet/IP Firmware: Specific Configuration Example
How would I configure this?
Using Dual Connect: Open a telnet or hyperterminal session (or other TCP/IP test tool) to view the plain ASCII data over a TCP port (specified by you in DMUP)

## Slide 35
EtherNet/IP Firmware: Specific Configuration Example
How would I configure this?
The LK-H2 software has been opened. (It’s connected via Ethernet port on the LK-G5000.)

## Slide 36
EtherNet/IP Firmware: Specific Configuration Example
How would I configure this?
Here the LK-H2 software can be seen receiving data at the same time as an EtherNet/IP PLC, and a (plain ASCII over TCP) Telnet session.

## Slide 37
EtherNet/IP Firmware: Specific Configuration Example
How would I configure this?
The LK-G5000 has been connected as shown above, with a Telnet session utilizing the Dual Connect option (plain ASCII now available on TCP/IP).

## Slide 38
Modbus/TCP Firmware: Specific Configuration Example
The embedded web page for the other DeviceMaster is opened, and Modbus TCP encapsulation begins…

## Slide 39
Modbus/TCP Firmware: Specific Configuration Example
The embedded web page for the other DeviceMaster is opened, and Modbus TCP encapsulation begins…

## Slide 40
Modbus/TCP Firmware: Specific Configuration Example
Once again, at the bottom of the configuration interface, an Application TCP connection is enabled.
(Dual Connect)

## Slide 41
Modbus/TCP Firmware: Specific Configuration Example
Matrikon OPC is opened and a Modbus TCP Master server is created. Specific Modbus IDs and addresses must be used in order to encapsulate plain ASCII data into Modbus.

## Slide 42
Modbus/TCP Firmware: Specific Configuration Example
The Matrikon OPC “tags” are successful. Also pictured is a Telnet session connecting via the “Dual Connect” Application TCP port.

## Slide 43
Multiple Firmware: Specific Configuration Example
And here we have two MBTCP Masters, an EtherNet/IP connection, and a telnet session ALL accessing the data from the ONE LK-G5000 RJ11 port. Simultaneously.

## Slide 44
EtherNet/IP Firmware: Specific Configuration Example
The LK-G5000 has been connected as shown above, with a Telnet session and Modbus TCP connected simultaneously with the EtherNet/IP PLC!

## Slide 45
4/30/2019
Control Room
Connecting the automation environment
INDUSTRIAL application
RFID Readers
Scanners
Weigh Scales
Printers
Sorters
Sensors
PLC
DeviceMaster
UP

## Slide 46: What is IO-Link?
IO-Link is a point-to-point serial communication protocol used to communicate with sensors and/or actuators

## Slide 47: IO-Link Master EIP-4 Highlights
Four channel IO-Link Master to EtherNet/IP
EtherNet/IP access to IO-Link sensor process, event and service data
  Class 1 (Implicit) and Class 3 (Explicit) interfaces
  Write-to-Tag/File, Read-from-Tag/File
Modbus TCP access to IO-Link sensor process, event and service data
Rugged IP67 housing with M12 connectors for harsh environments
DLR for fast network recovery
Windows app and web GUI for configuration and diagnostics
Wide operating temperature (0° to +70°C)
LEDs for device, network and port status
Additional digital input on every port
Powerful web configuration
IO-Link V1.1 compatibility
IO-Link COM1, COM2 and COM3 support (230K baud rate)
Slim-line machine-mount installation
Innovative QuickLinx technology

## Slide 48
IO-Link Master Features
Rugged IP67 machine mount design
Multi-side LED visibility
Four M12 IO-Link ports supporting COM3 (230K) connection
Two M12 Ethernet connectors with DLR support for sub-millisecond network recovery
EtherNet/IP support for ControlLogix, CompactLogix, MicroLogix, SLC, PLC5 PLCs and more
Each IO-Link port supports an auxiliary digital input on pin 2
Rotary switches for optional manual IP configuration
Bus through power for easy deployment

## Slide 49
Enjoy the flexibility of simultaneously connecting both EtherNet/IP and Modbus TCP based controllers to IO-Link devices.
Provide simultaneous access to the PLC and the HMI
Simultaneously control and monitor with a variety of systems
Simultaneously Provide IO-Link
Device Access to Multiple Controllers

## Slide 50
HMI Demo Interface Screen Shots

## Slide 51: Customers that Benefit from Comtrol’s Connectivity Technology
Industries
Factory Automation
Process Automation
Food and Beverage
Energy
Consumer Packaging
Automotive Manufacturing
Pharmaceutical

## Slide 52
100 Fifth Avenue NW
New Brighton, MN 55112
763.494.4100
sales@comtrol.com
www.comtrol.com